## Slide 1: Revision Information
130930-01/ Sean Yi

## Slide 2
ID | 1-1 | Name | State Machine |  | Rev. | 130930-01
▶rPanel-AllegroDog MFC-based GUI program ▶Control Program Real-time control callback
Shared Memory
Control Program
rPanel-AllegroDog
500 Hz
Data Sync. Event
-GUI
-Send command
-Status monitoring
-Real-time graph
-Real-time control callback
-Device I/O
-CAN communication
500 Hz
Status
Status
Shared Memory
Command
500 Hz

## Slide 3
ID | 1-1 | Name | State Machine |  | Rev. | 130930-01
▶INIT Just program started Servo off ▶HOMING Servo on Position servo mode enabled Homing process activated After homing the state will transit to READY state automatically Once homing was done, homing process is skipped and will transit to READY state ▶READY Servo on Position servo mode enabled Re-calculate encoder offsets Joints will be controlled to pre-defined position ▶OPERATION Servo on Current servo mode enabled Periodic communication on ▶STOP Emergency stop Servo off Periodic communication off
HOMING
READY
OPERATION
STOP
INIT
Home
Stop
Stop
Stop
Enable
Init

## Slide 4
ID | 1-1 | Name | Sub-state Machine (in OPERATION state) |  | Rev. | 130930-01
▶READY ▶HOP ▶WALK ▶
HOP
WALK
STOP
READY
OPERATION

## Slide 5
ID | 1-1 | Name | State Machine |  | Rev. | 130930-01
HOME
READY
OPERATION: HOP/ WALK
STOP
ENABLE
▶ENABLE CAN-ON (devCAN[0]->on(); devCAN[1]->on();) Activate-Controller (ActivateController(control_pid);)
▶HOME Servo on: Motors On by CAN devices (ServoOn();) ServoOn Controller (ServoOnController(control_pid);) Position servo mode enabled (devCAN->command(CAN_CMD_OPMODE_POSITION, 0, NULL, -1);) Homing process activated: all 12 motors do homing at the same time. (devCAN->command(CAN_CMD_SET_POS_MAX_VELOCITY, 100, NULL, -1);) (devCAN->command(CAN_CMD_HOMING, 0, NULL, -1);)
▶READY Set CURRENT-mode for all motors in CAN devices: devCAN->command(CAN_CMD_OPMODE_CURRENT, 0, NULL, -1); Set CURRENT-mode for all motors: (devMotor[i]->command(ALLEGRODOGMOTOR_CMD_OPMODE_CUR, 0, NULL, i)) Torque values from Allegrowalk class by Inversekinematic will be sent to motors.
▶HOP/WALK Set CURRENT-mode for all motors in CAN devices: devCAN->command(CAN_CMD_OPMODE_CURRENT, 0, NULL, -1); Set CURRENT-mode for all motors: (devMotor[i]->command(ALLEGRODOGMOTOR_CMD_OPMODE_CUR, 0, NULL, i)) Torque values from Allegrowalk class by Inversekinematic will be sent to motors.
▶STOP Motors-off(ServoOff();) Deactivate all drivers (“PPE!”)

## Slide 6
ID | 1-1 | Name | rPanel-AllegroDog |  | Rev. | 130930-01
▶[STOP] button Emergency stop ▶[HOME] button Start homing process ▶[ENABLE] button Enable operation(user defined controller) [READY] button: [HOP] button [WALK] button ▶
HOME
ENABLE
READY
HOP
WALK
STOP